## Slide 1
Forest Fire Detection
Using a LoRa Wireless Sensor Network
Six Raspberry Pi nodes · two-cluster multi-hop topology · TDMA scheduling
Nishank Swamy
Final Year Project · September 2026
Notes: Ground-based fire detection. Six Pis, LoRa radio, multi-hop. The two things I want to land today: collisions and routing dead ends are eliminated by construction, not by retrying.

## Slide 2
THE PROBLEM
Detection delay decides how much burns
Fire spreads faster than it is found. Area affected grows roughly with the square of elapsed time in the early phase, so cutting detection from hours to minutes has a disproportionate effect on final size.
1
Satellite thermal
Wide coverage, but revisits a few times a day and cloud blocks it entirely
2
Watchtower / camera
Continuous, but needs line of sight and only sees a plume once it clears the canopy
3
Ground sensors
Detect temperature rise, humidity collapse and combustion gas AT the origin — before a plume forms
The catch
Forest interiors have no cellular coverage and no mains power.
Ground sensing only works if the communication problem is solved first. That is what this project is actually about.
~5 km
LoRa range,
open terrain
2.4 kbps
air rate at
that range
Very low data rate for very long range — which suits telemetry, where a reading is a handful of bytes.
Notes: Three approaches. Ground sensing wins on latency but loses on communication — no cell, no mains. LoRa solves it: kilometres of range at battery power, in exchange for a data rate that would be useless for anything except sensor readings.

## Slide 3
OBJECTIVES
What the system has to do
1
Sense
Temperature, humidity and smoke at distributed points, with the fire decision made on the node itself
2
Reach
Deliver to a gateway with no cellular or mains infrastructure — including from nodes out of gateway range
3
Never collide
Multiple nodes share one radio channel. Packet collisions must be impossible, not merely unlikely
4
Never dead-end
A reading with a valid path to the gateway must not be lost to a routing dead end
5
Survive failure
A cluster head going down must not take its whole cluster off the map
6
Last on battery
Energy consumption low enough that battery operation is viable
Notes: Six objectives. Three and four are the interesting ones — note the wording: impossible, not unlikely. That distinction drives every design choice that follows.

## Slide 4
SYSTEM ARCHITECTURE
Six Pis, two clusters, three hops
2
3
CH-A
CH-B
5
GATEWAY
relay CH-B → CH-A
CLUSTER A
CLUSTER B
CH-B sits outside gateway range on purpose
Without it, head-to-head forwarding would never be exercised and the multi-hop capability would go untested. Node 5 reaches the gateway in three hops:
5 → CH-B → CH-A → GW
Notes: Two clusters. Members report to their head, heads forward to the gateway. CH-B is deliberately out of gateway range — that is what makes the relay real rather than decorative. Node 5 takes three hops.

## Slide 5
HARDWARE
Per node, and the traps in it
Raspberry Pi 4
gateway, 2 heads, 3 nodes
× 6
SX1262 868M LoRa HAT
UART, private point-to-point
× 6
DHT22
temperature + humidity
× 5
MQ-2
smoke / combustible gas
× 5
MCP3008
ADC over SPI
× 5
!
The Pi has no analogue input
The MQ-2’s analogue output cannot be read directly — hence the MCP3008 over SPI.
!
5 V sensor into a 3.3 V ADC
The MQ-2 runs on 5 V and its output can exceed 3.3 V, which would destroy the MCP3008. A divider is mandatory.
!
Jumper caps must come off
The HAT’s mode pins read HIGH when uncapped. With caps fitted the Pi cannot control radio power at all.
!
866 MHz, not 868
India licenses 865–867 MHz. 868 is the European band — the module is tunable, the marketing name is not the channel.
Notes: Bill of materials on the left. On the right, four constraints that each cost time to discover. The 5 V into 3.3 V one destroys hardware if missed.

## Slide 6
THE TWO HARD PROBLEMS
Both solved by construction, not by retry
Collisions
THE PROBLEM
Multiple nodes, one channel. Two transmissions overlapping in time corrupt each other.
OUR ANSWER
TDMA superframe
Every transmission occupies a slot owned by exactly one radio. Overlap is structurally impossible.
✓
0 collisions in 184 transmissions
Local minima
THE PROBLEM
Greedy geographic routing stalls where no neighbour is closer to the sink — even when a path exists.
OUR ANSWER
Explicit routing tables
No geometric decision is made, so there is no minimum to reach. Ordered fallbacks repair broken links.
✓
Cannot arise — proven by design
Notes: This is the core of the project. Note the framing on both: not "we retry until it works" but "the failure cannot occur". That is a stronger claim and it is the one I can defend.

## Slide 7
DESIGN DECISION 1
Why TDMA and not carrier sense
CSMA would not have worked here — and the reason is specific, not general.
2
CH-A
CH-B
node 2 and CH-B cannot hear each other
Both are heard by CH-A. Under CSMA, node 2 senses a clear channel — because it genuinely cannot hear CH-B transmitting — and keys up. Both collide at CH-A. Carrier sense cannot prevent this: the information needed is not available at the sensing node.
What slots buy
Collisions impossible by construction
No contention window, no backoff, no wasted carrier sensing
Radios can sleep on a schedule — the entire energy story
A slot map is a static object that can be verified before deployment
Cost: time synchronisation, and a fixed known node set. Both acceptable at six nodes.
Notes: The hidden terminal pair is the whole argument. If asked why not CSMA — node 2 and CH-B are mutually deaf but both heard by CH-A. Carrier sense is blind to exactly the case that matters.

## Slide 8
THE SCHEDULE
One superframe: 60 seconds, ten slots
0
GW
beacon broadcast
1
CH-A
rebroadcast beacon
2
CH-B
rebroadcast beacon
3
CH-A
own reading → GW
4
node 2
reading → CH-A
5
node 3
reading → CH-A
6
CH-B
own reading → CH-A
7
node 5
reading → CH-B
8
CH-B
forward cluster B
9
CH-A
forward everything
20 s of slots
40 s asleep
Why three beacon slots?
Cluster B is out of gateway range by design — so it cannot hear the sync beacon either. An unsynchronised node drifts until it transmits into someone else’s slot, reintroducing exactly the collisions TDMA prevents.
Sync is relayed along the same tree the data takes. Each relay needs its OWN slot: two heads rebroadcasting in one slot would collide with each other.
Duty cycle by role
member node
6.7%
backup head
10.0%
CH-B
16.7%
CH-A
30.0%
Notes: Ten slots, twenty seconds of activity, forty asleep. If asked why the beacon needs relaying: cluster B cannot hear the gateway, so it cannot hear the gateway’s clock either. Sync follows the data tree.

## Slide 9
DESIGN DECISION 2
The local minimum, with real numbers
Greedy geographic routing forwards to whichever neighbour is closest to the gateway. It needs no routing tables. It also fails.
Node N-03 is 714 m from the gateway. Its neighbours:
N-11
726 m
N-16
889 m
N-21
1025 m
N-24
1101 m
N-29
1214 m
714 m — where we are
Every neighbour is farther away.
Greedy has nothing to pick. The packet is stuck — and a perfectly good route exists:
N-03 → N-21 → N-08 → GW
That first hop goes 311 m in the WRONG direction. Greedy will never choose it, because greedy only ever moves closer.
Escaping a void requires moving away from the destination first.
Notes: Real numbers from the 50-node simulator. N-03 at 714 m, every neighbour farther. The working route starts by going 311 m backwards, which greedy cannot do by definition.

## Slide 10
THE CENTRAL FINDING
Protocol choice is scale-dependent
The right answers at six nodes are the OPPOSITE of the right answers at fifty. Both were built, so the trade is measured rather than assumed.
6 nodes — the hardware
Channel access
Static TDMA slots
Routing
Explicit next-hop tables
Roles
Fixed, surveyed in advance
Local minima
Cannot arise — no greedy decision
Five nodes cannot usefully negotiate. A fixed map is verifiable before deployment and cannot diverge.
50 nodes — the simulator
Channel access
Contention-based
Routing
Greedy geographic + perimeter
Roles
Elected, rotated by residual energy
Local minima
Occur, and must be recovered from
Static slots do not scale. Most nodes are out of sink range, so geographic forwarding earns its keep.
Notes: If asked why the two halves of the project use contradictory techniques — this slide is the answer. It is not inconsistency, it is the finding. Contention and greedy routing are correct at scale and actively harmful at six nodes.

## Slide 11
RQ5 + RQ7 — ENERGY
The radio is 1% of the problem
The standard WSN energy model accounts for the transceiver. On this hardware the transceiver is a rounding error — so every optimisation in this project acts on 1% of the budget.
Where the watts go — CH-A
Pi platform
53%
MQ-2 heater
45.4%
LoRa radio
1.2%
DHT22
0.5%
RQ5 — is the standard model valid here?
Applied unmodified it predicted ZERO node deaths in 400 rounds.
1450x
overstatement of
battery life
Answer: no. A Pi is not a mote.
RQ7 — is battery operation viable?
As built
2.7 h
Radio sleep OFF
2.6 h
No MQ-2
7.0 h
MCU + no MQ-2
21.8 h
Disabling the radio sleep — the mechanism this project is built around — costs 4%. Removing the gas sensor is worth 3x. NOT viable as built, and the blocker is not the network.
Notes: This is the strongest negative result. The radio is 1.2% of node power, so TDMA sleep — the centre of this project — is worth 4%. If asked whether that invalidates the work: no, it relocates it. The networking contribution stands; the energy claim has to be about the whole node.

## Slide 12
RESILIENCE
What happens when something breaks
1
Link fails
Acknowledged forwarding, three retries, then fall through to the next hop in the ordered route table.
2
Cluster head dies
Its backup detects unacknowledged uplinks and promotes itself — adopting the dead head’s slots, which are free precisely because it is silent.
3
No route at all
Store and forward. The reading is buffered, not discarded, and retried next frame.
4
Operator needs it stopped
A command field in the beacon — the network’s only downlink. Halt auto-expires after 30 minutes.
A halted fire-detection network is a silent one — so the stop command has a dead-man timer at both ends.
Notes: Four failure modes and the response to each. The halt auto-expiry is worth calling out as a safety property — a latched stop that someone forgets to clear is worse than the problem it solves.

## Slide 13
VERIFICATION
Testing that actually found things
The deployment firmware, on a virtual radio
netsim.py imports the actual gateway.py and sensor_node.py rather than reimplementing them, and runs all six stacks against a channel that models airtime, range and overlap. What is tested is what ships.
1
Truth test on a hop address
The gateway’s address is 0 — falsy in Python. Every successful delivery read as failure; heads re-queued delivered readings forever.
2
No beacon relay
Cluster B, out of gateway range by design, could never synchronise.
3
Listen slots hand-listed
CH-A slept through CH-B’s transmission slot. Its readings had nowhere to land.
4
Failover on beacon silence
A backup seized the slots of a working head — 48 collisions.
5
Halt severed the relay
A halted CH-A stopped relaying the beacon, cutting cluster B off from the command channel entirely.
5 defects
found before any hardware was connected
Two would have presented on hardware as intermittent data loss — the hardest class of fault to diagnose in a forest. One would have appeared only under head failure, which is exactly the condition the mechanism exists to handle.
Notes: The strongest slide in the deck. Most projects claim testing; this shows testing that found something. Be ready to walk through the falsy-zero bug in detail — it is the most instructive.

## Slide 14
RESULTS — SIMULATED
Eight frames, six nodes
0
collisions in 184
transmissions
100%
packet delivery,
40 of 40 readings
0
duplicates and
0 retries
3
hops for node 5,
via CH-B and CH-A
Delivery path per node
CH-A
1 → GW
1 hop
node 2
2 → 1 → GW
2 hops
node 3
3 → 1 → GW
2 hops
CH-B
4 → 1 → GW
2 hops
node 5
5 → 4 → 1 → GW
3 hops
Fault injection
Fire at node 5 propagated across all three hops, flagged correctly, zero collisions
CH-A killed: node 3 promoted after three unacknowledged frames, adopted its slots, zero collisions through failover
Cluster B correctly partitioned and buffered — no algorithm can cross a physical partition
Every figure regenerated by python3 pi/tools/experiments.py
Notes: Headline numbers. Point at the footer: these are reproducible from the repo, not copied from a notebook. If asked about the partition case — that is correct behaviour, not a failure. CH-B can only hear CH-A and node 5, so when CH-A dies cluster B is physically cut off. Buffering is the right answer.

## Slide 15
LIVE DEMONSTRATION
What I will show you
1
Topology on the map
Cluster heads ringed in blue, backups dashed, members linked to their head. The gateway at the centre.
2
A three-hop route
Select node 5 — its path draws as 5 → CH-B → CH-A → gateway, coloured per hop.
3
Local minima recovery
On the 50-node view, a node outlined amber. Its route detours around the ridge in perimeter mode.
4
Cluster head failover
Kill a head. Within three rounds its backup is promoted, the cluster re-homes, the event log records it.
5
Emergency stop
Halt the network. The banner goes red and every node stops transmitting — then auto-resumes.
Two views, one dashboard
A single interface abstracts the data origin, so the same rendering code serves the simulator and the live gateway. Switching between them is one line in the markup.
SIMULATED
50 nodes, clustering and geographic routing at a scale where they earn their keep
LIVE
Real telemetry from the gateway Pi, with the true multi-hop path drawn from the packets themselves
Notes: Demo running order. Have the dashboard already open before starting. The failover and the halt are the two that always land — they are visibly dynamic rather than static screenshots.

## Slide 16
IN CLOSING
Two claims I can defend
1
Collisions and routing dead ends are eliminated by construction
TDMA slots make overlap structurally impossible; explicit routing tables leave no geometric decision that could stall. Neither is a retry mechanism.
2
Protocol choice is scale-dependent, and I measured it
The correct techniques at six nodes are the opposite of those at fifty. Building both makes that a finding rather than an assumption.
Next
Microcontroller sensor nodes to escape the Pi’s 0.35 W sleep floor · solar harvesting · adaptive frame length · sensor fusion across neighbours · alert integration with forest department
github.com/nishankswamy/forest-fire-dashboard
Notes: Close on the two claims. Then invite questions — the areas I expect are why TDMA over CSMA, why the two halves differ, and whether the simulator results transfer to hardware. Honest answer to the last one: they verify logic, not radio behaviour.